CISCO PACKET TRACER

Prepared By: Er. Sharat Maharjan, Prime College

Lab 1: Creating a Peer-to-Peer Network

- Equipment needed
  - 2 Workstations
  - 1 Ethernet cable
- Identify the cable (straight through or cross over) and connect the workstations I.e; PC1 and PC2.
- Configure the layer 3 address to the workstations
  - PC1-- 192.168.1.1/24
  - PC2-- 192.168.1.2/24
- Verify Connectivity (ping command)
  - Ping PC2 from PC1.

Lab 2: Implement the LAN Topologies

Topology 1: Star Topology

Device	Interface	IPv4 Address	Subnet Mask
Host1	NIC	192.168.10.101	255.255.255.0
Host2	NIC	192.168.10.102	255.255.255.0
Host3	NIC	192.168.10.103	255.255.255.0
Server1	NIC	192.168.10.104	255.255.255.0

- Design the given topology.
- Configure the layer 3 address to all nodes according to addressing table.
- From the command prompt on each node, run the ping test and write the output.
  - Can Host1 ping Server1?
  - Can Server1 ping Host3 and Host2?

Topology 2: Bus Topology

Device	Interface	IPv4 Address	Subnet Mask	Switch
Host1	NIC	192.168.11.101	255.255.255.0	Switch1
Host2	NIC	192.168.11.102	255.255.255.0	Switch2
Host3	NIC	192.168.11.103	255.255.255.0	Switch3
Server1	NIC	192.168.11.104	255.255.255.0	Switch4

- Design the given topology.
- Assign the IP address to all nodes according to addressing table.
- From the command prompt on each node, run the ping test and write the output.
  - Can Host1 ping Server1?
  - Can Server1 ping Host3 and Host2?

Topology 3: Ring Topology

Device	Interface	IPv4 Address	Subnet Mask	Switch
Host1	NIC	192.168.100.101	255.255.255.0	Switch1
Host2	NIC	192.168.100.102	255.255.255.0	Switch2
Host3	NIC	192.168.100.103	255.255.255.0	Switch3
Server1	NIC	192.168.100.104	255.255.255.0	Switch4

- Design the given topology.
- Assign the IP address to all nodes according to addressing table.
- From the command prompt on each node, run the ping test and write the output.
  - Can Host1 ping Host3?
  - Can Server1 ping Host2?